## Slide 1
Boundary conditions and volume flow
Mean inlet speed: 2.0 mm/s | Imposed conditions and computed flow rates
Boundary | Pressure / traction BC (Pa) | Volume flow (µL/min) | Flow relative to inlet
Inlet | Not prescribed (flow inlet) | 9.308 × 10⁻⁴ | 100%
Outlet 01 | 0 (zero traction) | 3.963 × 10⁻⁵ | 4.26%
Outlet 02 | 0 (zero traction) | 7.931 × 10⁻⁴ | 85.21%
Outlet 03 | 0 (zero traction) | 9.808 × 10⁻⁵ | 10.54%
BC = boundary condition. Inlet: prescribed flow; outlets: zero traction (Neumann).
The flow columns show computed magnitudes. Zero traction does not impose zero nodal pressure.
Notes: 本表按用户要求显示施加的边界条件。入口采用 Dir + Impose_flux，指定流量，不指定压力；三个出口采用 Neu + Value=0，即零法向牵引边界（Pa）。出口的 0 是边界载荷设置，不是求解得到的截面平均压力，也不是压力节点强制为零。流量列及比例仍为当前 mean-2p0-mmps 工况 step 71 的计算结果；流量换算因子为 6 × 10^10 µL/min per m³/s。各出口比例分别四舍五入后合计 100.01%。Boundary conditions were read from the actual solver.xml; no solver parameters were changed.